## Slide 1
Brian Watts, Ph.D.
BIA Core Facility
October 5-8, 2020
BIA Core SPR Results
Spyros Pavlidis
RNA Aptamers
BSA
Histone, Calf Thymus

## Slide 2
Instrument Preparation
Completed Desorb and Sanitize cleaning procedure x 1 and Desorb procedure using RNase Away x 3.
System run on standby with Milli-Q Water as running buffer for several days to rinse system.
RNA Aptamer Immobilization
Immobilized thiolated RNA aptamer via incubation on a blank Au sensor chip.
  RNA Immobilization: 1 µM RNA aptamer; 18,000 sec x 3 @ 1 µL/min on Fc4 (15 hr incubation)
  Spacer Immobilization: 1 mM 6-Mercapto-1-hexanol (MCH); 18,000 sec @ 1 µL/min on Fc3,4 (5 hr incubation)
Analyte Preparation
Weighed out ~10 mg of dry Calf Thymus Histone (CTH) and Bovine Serum Albumin (BSA) and solubilized in 2 mL HBS-EP+.
Measured concentration via nanodrop for BSA (MW = 66,500 g/mol, ε = 43,824 M-1cm-1) and CTH (MW = 14,956 g/mol, ε = 5,376.5 M-1cm-1) stocks.
Binding Screen
Manually identified ideal regeneration condition via sequential injection.
Set up method to screen BSA and CTH against MCH and RNA/MCH surfaces.
  Flow Cells: 3,4 (Ref sub. 4-3)
  Binding: 180 sec association, 600 sec dissociation @ 30 µL/min
  Regeneration: 50 mM NaOH, 1 M NaCl, 60 sec @ 30 µL/min (30 sec baseline stabilization)
  Exp 1: 0, 1.56, 3.13, 6.25, 12.5, 25, 50, 100, 200 nM BSA
  0, 1.35, 2.71, 5.41, 10.8, 21.7, 43.3, 86.3, 173.2 nM CTH*
  Exp 2: 0, 0.10, 0.20, 0.39, 0.78, 1.56, 3.13, 6.25, 12.5, 25, 50, 100 nM BSA
  0, 0.10, 0.20, 0.39, 0.78, 1.56, 3.13, 6.25, 12.5, 25, 50, 100 nM CTH
Experimental Details
(SPR – Biacore T200)
BEW
*CTH dilutions for Exp 1 were originally made to match BSA dilutions, however recalculation of the MW and ε of CTH reduced the calculated stock concentration and subsequent dilutions.

## Slide 3
-2
3
8
13
18
-100
0
100
200
300
400
500
600
700
800
Response (RU)
Time (s)
MCH Surface (Fc3, Raw)
Buffer Subtracted
200 nM BSA
100 nM BSA
50 nM BSA
25 nM BSA
12.5 nM BSA
6.25 nM BSA
3.125 nM BSA
1.5625 nM BSA
0 nM BSA
-2
0
2
4
6
8
10
12
14
16
18
-100
0
100
200
300
400
500
600
700
800
Response (RU)
Time (s)
RNA Surface (Fc4. Raw)
Buffer Subtracted
200 nM BSA
100 nM BSA
50 nM BSA
25 nM BSA
12.5 nM BSA
6.25 nM BSA
3.125 nM BSA
1.5625 nM BSA
0 nM BSA
BSA Binding Results (Exp 1)
-3.5
-3
-2.5
-2
-1.5
-1
-0.5
0
0.5
1
1.5
-100
0
100
200
300
400
500
600
700
800
Response (RU)
Time (s)
RNA Surface (Fc4-3, Ref. Sub.)
MCH Surface Subtracted, Buffer Subtracted
200 nM BSA
100 nM BSA
50 nM BSA
25 nM BSA
12.5 nM BSA
6.25 nM BSA
3.125 nM BSA
1.5625 nM BSA
0 nM BSA
Purpose
Determine if specific binding of BSA to MCH and RNA surfaces is observed.
Results
No BSA binding detected to either MCH or RNA surfaces

## Slide 4
-20
30
80
130
180
-100
0
100
200
300
400
500
600
700
800
Response (RU)
Time (s)
MCH Surface (Fc3, Raw)
Buffer Subtracted
173.2 nM CTH
86.6 nM CTH
43.3 nM CTH
21.65 nM CTH
10.825 nM CTH
5.4124 nM CTH
2.7062 nM CTH
1.3531 nM CTH
0 nM CTH
CTH Binding Results (Exp 1)
-50
0
50
100
150
200
250
300
-100
0
100
200
300
400
500
600
700
800
Response (RU)
s
Time (s)
RNA Surface (Fc4-3, Ref. Sub.)
MCH Surface Subtracted, Buffer Subtracted
173.2 nM CTH
86.6 nM CTH
43.3 nM CTH
21.65 nM CTH
10.825 nM CTH
5.4124 nM CTH
2.7062 nM CTH
1.3531 nM CTH
0 nM CTH
Purpose
Determine if specific binding of CTH to MCH and RNA surfaces is observed.
Results
Observed CTH binding to both MCH and RNA surfaces.
CTH binding to MCH surface weaker than binding to RNA surface.
Suggests detection of specific binding of CTH to the RNA surface
Binding curve morphology degraded at higher concentrations likely due to saturation of the surface binding sites resulting in aggregation and/or aberrant signal changes.
-50
50
150
250
350
450
-100
0
100
200
300
400
500
600
700
800
Response (RU)
Time (s)
173.2 nM CTH
86.6 nM CTH
43.3 nM CTH
21.65 nM CTH
10.825 nM CTH
5.4124 nM CTH
2.7062 nM CTH
1.3531 nM CTH
0 nM CTH
RNA Surface (Fc4, Raw)
Buffer Subtracted

## Slide 5
 |  | MCH (Fc3) | RNA (Fc4) | RNA - MCH (Fc4-3) | [RNA - MCH] - BSA
Analyte | Conc (nM) | Resp (RU) | Resp (RU) | Resp (RU) | Resp (RU)
CTH | 0 | 12.5 | 11 | -1.4 | -0.85
CTH | 1.35 | 23.5 | 31.7 | 8.2 | 9.7
CTH | 2.71 | 25.6 | 46.2 | 20.6 | 22
CTH | 5.41 | 32.7 | 71.8 | 39.1 | 40.8
CTH | 10.8 | 47.3 | 111.9 | 64.6 | 66.1
CTH | 21.7 | 72.8 | 159.8 | 87 | 88.8
CTH | 43.3 | 108.8 | 240.1 | 131.3 | 124.25
CTH | 86.6 | 157.4 | 319.2 | 161.8 | 163.5
CTH | 173.2 | 170.9 | 459.7 | 288.8 | 290.8
CTH | 0 | 20.5 | 17.2 | -3.3 | -1.6
CTH | 43.3 | 130 | 242 | 112.1 | 115.4
BSA | 0 | 12.3 | 11 | -1.3 | --
BSA | 1.56 | 17.1 | 15.7 | -1.5 | --
BSA | 3.13 | 17.6 | 16.2 | -1.4 | --
BSA | 6.25 | 17.9 | 16.2 | -1.7 | --
BSA | 12.5 | 23.3 | 21.7 | -1.5 | --
BSA | 25 | 21.6 | 19.9 | -1.8 | --
BSA | 50 | 19.9 | 18 | -1.8 | --
BSA | 100 | 25.1 | 23.4 | -1.7 | --
BSA | 200 | 29.8 | 27.8 | -2 | --
BSA | 0 | 19 | 17.2 | -1.7 | --
BSA | 50 | 28.2 | 24.9 | -3.3 | --
Binding Results Summary (Exp 1)
MCH and RNA Binding Response (Raw)
RNA Binding Response (MCH Cont. Surf. Subtracted)
RNA Binding Response
(MCH Cont. Surf., BSA Cont. Subtracted)
CTH
BSA
CTH
BSA
Results
1.35 nM is lowest concentration that produced detectable binding signal

## Slide 6
Binding Kinetics Results (Exp 1)
-20
0
20
40
60
80
100
120
140
160
-100
0
100
200
300
400
500
600
700
800
Response (RU)
Time (s)
1:1 Binding Model
ka (1/Ms) | kd (1/s) | Kd (M) | Kd (nM) | Chi2 (RU2)
2.59E+06 | 1.06E-03 | 4.08E-10 | 0.4 | 9.73
Results
Appropriate kinetics/affinity calculations require purified, homogeneous solutions of biomolecules with accurately determined concentrations.
Due to the CTH analyte being a mixture of 5 different histone proteins, obtaining a true measure of the kinetics and affinity of the CTH-RNA interaction is not possible.
The binding curves obtained in this assay are a result of the complex combination of association, dissociation, and competition interactions of the 5 histone proteins with the RNA surface.
While a dose-dependent CTH binding response is observed, the obtained binding curves are poorly fit by the 1:1 binding model (Chi2 = 9.73 RU2). The poor fit is not surprising considering the heterogeneity of the analyte.
The apparent affinity for the bulk interaction between CTH and the RNA surface can be calculated (assuming the concentration used for CTH was determined appropriately).
43.3 nM CTH
21.65 nM CTH
10.825 nM CTH
5.4124 nM CTH
2.7062 nM CTH
1.3531 nM CTH
RNA Surface (Fc4-3, Ref. Sub.)
MCH Surface Subtracted, Buffer Subtracted

## Slide 7
Binding Results Summary (Exp 2)
-50
0
50
100
150
200
-100
0
100
200
300
400
500
600
700
800
Response (RU)
Time (s)
12.5 nM CTH
6.25 nM CTH
3.13 nM CTH
1.56 nM CTH
0.78 nM CTH
0.39 nM CTH
0.20 nM CTH
0.10 nM CTH
0 nM CTH
25 nM CTH
50 nM CTH
100 nM CTH
RNA Surface (Fc4-3, Ref. Sub.)
MCH Surface Subtracted, Buffer Subtracted
-5
-4
-3
-2
-1
0
1
2
3
-100
0
100
200
300
400
500
600
700
800
Response (RU)
Time (s)
12.5 nM CTH
6.25 nM CTH
3.13 nM CTH
1.56 nM CTH
0.78 nM CTH
0.39 nM CTH
0.20 nM CTH
0.10 nM CTH
0 nM CTH
25 nM CTH
50 nM CTH
100 nM CTH
RNA Surface (Fc4-3, Ref. Sub.)
MCH Surface Subtracted, Buffer Subtracted
BSA
CTH
Purpose
Determine lower limit of detection of CTH binding to an RNA surface.
Results
No BSA binding detected to either MCH or RNA surfaces
CTH binding again observed to both MCH and RNA surfaces
RNA surface appears to have degraded demonstrated by the overall lower CTH-RNA binding responses, higher CTH-MCH binding responses, and poor curve morphology.
Unable to define an LOD lower than the previously measured 1.35 nM CTH.

## Slide 8
 |  | MCH (Fc3) | RNA (Fc4) | RNA - MCH (Fc4-3) | [RNA - MCH] - BSA
Conc (nM) | Analyte | Resp (RU) | Resp (RU) | Resp (RU) | Resp (RU)
CTH | 0 | 8.9 | 7.4 | -1.5 | -0.4
CTH | 0.10 | 18.9 | 16.7 | -2.2 | -0.2
CTH | 0.20 | 20.1 | 17.5 | -2.7 | -0.8
CTH | 0.39 | 23.8 | 20.6 | -3.3 | -1.5
CTH | 0.78 | 35.3 | 31.7 | -3.5 | -1.1
CTH | 1.56 | 37.4 | 32.6 | -4.8 | -3.1
CTH | 3.13 | 50.4 | 44.5 | -5.9 | -4
CTH | 6.25 | 78.7 | 81.2 | 2.5 | 4.6
CTH | 12.5 | 124.1 | 155.5 | 31.4 | 33.7
CTH | 25 | 169 | 232.5 | 63.4 | 76.45
CTH | 50 | 226.6 | 344.7 | 118.1 | 120.8
CTH | 100 | 323.8 | 437.2 | 113.4 | 117.7
CTH | 25 | 115.7 | 199 | 83.3 | 87.2
CTH | 0 | 18.3 | 14.9 | -3.4 | -1.4
BSA | 0 | 12.4 | 10.3 | -2.1 | --
BSA | 0.10 | 21.7 | 19.7 | -2 | --
BSA | 0.20 | 22.6 | 20.8 | -1.9 | --
BSA | 0.39 | 19.8 | 17.9 | -1.8 | --
BSA | 0.78 | 22.8 | 20.4 | -2.4 | --
BSA | 1.56 | 17.5 | 15.8 | -1.7 | --
BSA | 3.13 | 22.9 | 20.9 | -1.9 | --
BSA | 6.25 | 21.7 | 19.6 | -2.1 | --
BSA | 12.5 | 27.6 | 25.3 | -2.3 | --
BSA | 25 | 17.6 | 15.3 | -2.3 | --
BSA | 50 | 23.3 | 20.6 | -2.7 | --
BSA | 100 | 24.6 | 20.4 | -4.3 | --
BSA | 25 | 28.6 | 24.7 | -3.9 | --
BSA | 0 | 20.4 | 18.4 | -2 | --
RNA Binding Response
(MCH Cont. Surf., BSA Cont. Subtracted)
RNA Binding Response (MCH Cont. Surf. Subtracted)
MCH and RNA Binding Response (Raw)
Binding Results Summary (Exp 2)
CTH
BSA
CTH
BSA