## Slide 1
Brian Watts, Ph.D.
BIA Core Facility
December 3, 2020
BIA Core SPR Results
Spyros Pavlidis
RNA Aptamer
BSA
Histone H3.2
Histone H4
Histone, Calf Thymus

## Slide 2
RNA Aptamer Immobilization
Immobilized thiolated RNA aptamer via incubation on a blank Au sensor chip.
  RNA Immobilization: 1 µM RNA aptamer; 18,000 sec x 4 @ 1 µL/min on Fc3 (20 hr incubation)
  Spacer Immobilization: 1 mM 6-Mercapto-1-hexanol (MCH); 18,000 sec @ 1 µL/min on Fc1,3 (5 hr incubation)
Binding Screen
Manually identified ideal regeneration condition via sequential injection.
Set up method to screen BSA and CTH against MCH and RNA/MCH surfaces.
  Flow Cells: 3,4 (Ref sub. 4-3)
  Binding: 180 sec association, 600 sec dissociation @ 30 µL/min
  Regeneration: 10 mM HCl, 60 sec @ 30 µL/min (60 sec baseline stabilization)
  Exp 1: 0, 200, 400 nM BSA
  0, 200, 400 nM H3.2
  0, 100, 200 nM H4
  0, 100, 200 nM CTH
Experimental Details
(SPR – Biacore T200)
BEW

## Slide 3
Ref Sub (Fc3-1)
MCH Surface (Fc1)
RNA Surface (Fc3)
Binding Results
Green curve is the raw sensorgram showing binding to the active, RNA surface.
Red curve is the raw sensorgram showing non-specific binding to the control, MCH surface.
Blue curve is the reference subtracted sensorgram showing specific binding to the RNA surface.
Regeneration portion of curve removed for clarity
Regeneration portion of curve removed for clarity
-50
0
50
100
150
-200
0
200
400
600
800
1000
1200
BSA 400 nM
Response (RU)
Time (s)
-50
0
50
100
150
-200
0
200
400
600
800
1000
1200
BSA 200 nM
Response (RU)
Time (s)
 |  | Binding Resp (RU)
Analyte | Conc | Fc1 | Fc3 | Fc3-1
BSA | 200 nM | 123.4 | 126.2 | 2.9
BSA | 400 nM | 119.8 | 122.1 | 2.4
The raw sensorgrams (green/red) show a sharp vertical bulk shift due to buffer effects with minimal non-specific binding that is nearly identical on both active and control surfaces.
Thus the reference subtracted curve shows minimal/no binding

## Slide 4
Ref Sub (Fc3-1)
MCH Surface (Fc1)
RNA Surface (Fc3)
Binding Results
Green curve is the raw sensorgram showing binding to the active, RNA surface.
Red curve is the raw sensorgram showing non-specific binding to the control, MCH surface.
Blue curve is the reference subtracted sensorgram showing specific binding to the RNA surface.
Regeneration portion of curve removed for clarity
Regeneration portion of curve removed for clarity
-200
0
200
400
600
800
1000
1200
1400
1600
1800
2000
-200
0
200
400
600
800
1000
1200
Histone H3.2 200 nM
Response (RU)
Time (s)
-200
0
200
400
600
800
1000
1200
1400
1600
1800
2000
-200
0
200
400
600
800
1000
1200
Histone H3.2 400 nM
Response (RU)
Time (s)
 |  | Binding Resp (RU)
Analyte | Conc | Fc1 | Fc3 | Fc3-1
H3.2 | 200 nM | 928.1 | 993.4 | 67.9
H3.2 | 400 nM | 1511.2 | 1800.2 | 292.6
The raw sensorgrams (green/red) show significant binding response that is slightly higher on the RNA surface.
H3.2 appears to show some slight binding to the RNA surface, but there is still significant non-specific/background binding of H3.2 to the MCH surface.
The ref sub curve has odd morphology due to the differing slopes.
Both surfaces show good removal of bound protein after regeneration (baseline at 1000 s is close to 0 RU).

## Slide 5
Ref Sub (Fc3-1)
MCH Surface (Fc1)
RNA Surface (Fc3)
Binding Results
Green curve is the raw sensorgram showing binding to the active, RNA surface.
Red curve is the raw sensorgram showing non-specific binding to the control, MCH surface.
Blue curve is the reference subtracted sensorgram showing specific binding to the RNA surface.
Regeneration portion of curve removed for clarity
Regeneration portion of curve removed for clarity
-500
0
500
1000
1500
2000
2500
3000
-200
0
200
400
600
800
1000
1200
Histone H4 100 nM
Response (RU)
Time (s)
-500
0
500
1000
1500
2000
2500
3000
-200
0
200
400
600
800
1000
1200
Histone H4 200 nM
Response (RU)
Time (s)
The raw sensorgrams (green/red) show significant binding response that is higher on the RNA surface.
H4 appears to show more binding to the RNA surface than H3.2, but there is still significant non-specific/background binding of H4 to the MCH surface.
The ref sub curve has odd morphology due to the differing slopes.
Both surfaces show good removal of bound protein after regeneration (baseline at 1000 s is close to 0 RU).
 |  | Binding Resp (RU)
Analyte | Conc | Fc1 | Fc3 | Fc3-1
H4 | 100 nM | 1958.3 | 2299.8 | 345.9
H4 | 200 nM | 2116.3 | 2588.7 | 473.6

## Slide 6
Ref Sub (Fc3-1)
MCH Surface (Fc1)
RNA Surface (Fc3)
Regeneration portion of curve removed for clarity
Regeneration portion of curve removed for clarity
Binding Results
Green curve is the raw sensorgram showing binding to the active, RNA surface.
Red curve is the raw sensorgram showing non-specific binding to the control, MCH surface.
Blue curve is the reference subtracted sensorgram showing specific binding to the RNA surface.
-200
0
200
400
600
800
1000
1200
1400
1600
-200
0
200
400
600
800
1000
1200
CTH 100 nM
Response (RU)
Time (s)
-200
0
200
400
600
800
1000
1200
1400
1600
-200
0
200
400
600
800
1000
1200
CTH 200 nM
Response (RU)
Time (s)
The raw sensorgrams (green/red) show significant binding response that is substantially higher on the RNA surface.
CTH appears to show binding to the RNA surface, but there is still significant non-specific/background binding of CTH to the MCH surface.
The ref sub curve has odd morphology due to the differing slopes.
Both surfaces show good removal of bound protein after regeneration (baseline at 1000 s is close to 0 RU).
 |  | Binding Resp (RU)
Analyte | Conc | Fc1 | Fc3 | Fc3-1
CTH | 100 nM | 599.4 | 1150.0 | 550.6
CTH | 200 nM | 806.3 | 1479.0 | 673.9

## Slide 7
Conclusions
Binding response appears strongest with H4, followed by CTH, then H3.2
For H3.2, H4, and CTH the raw curves look alright, but the reference subtracted curves have odd morphology. This is due to the differing slopes of the control and active flow cells. It is possible that these differing slopes indicate that different binding interactions are occurring on each flow cell. Conceivably, the control flow cell is showing non-specific binding between the histone and the “blank” MCH surface whereas the active flow cell is showing specific binding between the histone and the RNA.
Seeing non-specific binding to a blank flow cell is not unusual, although typically the accumulation of protein on the blank surface forms a layer after the first one or two cycles and any interference from the non-specific binding is mitigated in subsequent cycles.
However in this case, I believe the issue may be due to a few factors:
  The control surface has more exposed gold as the MCH alone doesn’t mask as much of the surface as the RNA plus the MCH, which allows the histones to bind non-specifically to exposed gold.
OR
  The MCH forms an amorphous, “sticky” layer on the blank gold surface to which the histone binds non-specifically and thus the MCH surface is not a good negative control for this experiment.
AND
  The regeneration conditions necessary to remove the histones from the RNA are strong enough that they actually remove any of the non-specifically adsorbed protein on the control flow cell, thus preventing the typical accumulation of protein on the blank surface resulting in large non-specific binding responses that don’t attenuate in subsequent cycles.
    This is supported by the fact that weaker regeneration conditions could partially regenerate the RNA surface with little to no impact on the control surface.

## Slide 8
The solution I propose is to order a thiolated, scrambled RNA or non-histone binding RNA aptamer of similar proportions to the experimental KU7 RNA aptamer. With that, we can generate a true control surface that will allow us to differentiate the specific RNA-histone interaction from the non-specific background binding.
If we are able to show that the binding responses observed on the RNA surface are solely due to the specific RNA-histone interaction, then we can forgo the use of a negative control surface and rely on a negative control analyte (BSA) as the reference.
Without the above information we wouldn’t be able to make a definitive conclusion that the binding responses we are seeing is a specific interaction between the histone and the KU7 RNA aptamer or non-specific binding of the histone to a generic RNA.
Conclusions (contd)